## Slide 1: Where Nepal's Climate Risk Lives
CAPSTONE PROJECT | OCTOBER 2026
A risk assessment of all 77 districts, tested against 15 years of recorded disasters, and a USD 100 million resilience recommendation
NEPAL CLIMATE RISK · INTELLIGENCE PLATFORM
PRESENTER / ANALYST
Kingsley Chigozie
Live app: nepal-climate-risk.streamlit.app
Notes: Good morning. My name is Kingsley Chigozie, and I carried out this analysis. This assessment answers one practical question: if a donor has 100 million dollars to make Nepal more resilient to climate disasters, where should it go and why? We look at all 77 districts, we test our answer against 15 years of real disaster records, and we end with a recommendation where every dollar is tied to evidence.

## Slide 2: 26 August 2026: a glacier collapse
THE EVENT
Trigger
Glacier and rock-and-ice collapse at high altitude
Path
Flash flood down the Bhote Koshi and Trishuli river corridor
Human cost
Significant loss of life and displacement
Assets
Damage to hydropower generation facilities
THE CENTRAL QUESTION
How do climate hazards, terrain, population, infrastructure and access interact to create risk across Nepal's 77 districts, and where has that risk actually materialized?
Notes: On 26 August 2026 a glacier and rock-and-ice collapse sent a flash flood down the Bhote Koshi and Trishuli rivers, north of Kathmandu. People died, families were displaced, and hydropower plants were damaged. This was not a one-off: Nepal has a long record of floods and landslides. So the question is bigger than this one event. Across all 77 districts, where is the risk, what drives it, and does Nepal's own disaster history agree with us?

## Slide 3: Risk exists only where three things meet
OUR APPROACH
Hazard
Heavy rain, steep terrain, big rivers
×
Exposure
People, hospitals, schools, hydropower
×
Vulnerability
Few roads, overstretched hospitals
1 MEASURE
Score all 77 districts on hazard, exposure and vulnerability
2 TEST
Compare scores with 12,341 recorded disasters (after cleaning), 2011-2026
3 INVEST
Allocate USD 100M, every dollar tied to a named finding
Notes: Disaster professionals define risk as hazard times exposure times vulnerability. A huge landslide on an empty mountainside is hazard without exposure: low risk. A city with no hazard is also low risk. Risk is high only where all three meet. Our method has three steps: measure those three ingredients for every district, test the result against real disasters, and then invest.

## Slide 4: Four datasets, four flaws fixed first
THE DATA
What we used
Climate: NASA POWER
Daily rainfall and temperature, 1990-2026
Terrain and rivers: HydroSHEDS
Elevation, river size, distance to rivers
Exposure: Census 2021, OpenStreetMap
Population, hospitals, schools, roads, hydropower
Disasters: BIPAD Portal
12,341 floods, landslides and rain events after removing duplicates
What we corrected
Rainfall doubles in 2004
A satellite data-source change, not climate. Trends use 2004-2025 only.
Only 45 of 77 rain series unique
Neighbouring districts share a satellite cell. Each counted once.
Slope data stuck near 90°
A unit error upstream. Elevation spread used instead.
2026 ends on 30 August
A partial year. Excluded from annual totals.
Notes: We used four public datasets. Before any analysis we read the data dictionary and fixed four problems. One: rainfall doubles overnight in 2004 because NASA changed its data source, so all trends start in 2004. Two: the satellite grid is coarse, so only 45 of the 77 rainfall series are actually different; we count each once. Three: the slope column has a unit error and shows almost 90 degrees everywhere, which is impossible, so we measure steepness with the spread of elevation instead. Four: 2026 stops at the end of August, so we don't treat it as a full year. We also fixed a spelling mismatch for Rukum district so the tables join correctly.

## Slide 5: Rainfall is rising about 22.1 mm a year
CLIMATE | 2004-2025
F1
Chart: Average annual rainfall, 45 independent series (mm)
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Annual rainfall | 1041 | 1075 | 1025 | 1243 | 1300 | 928 | 1117 | 1235 | 1034 | 1452 | 1210 | 1232 | 1247 | 1216 | 1160 | 1314 | 1651 | 1784 | 1431 | 1285 | 1502 | 1417
Trend | 1036 | 1058 | 1081 | 1103 | 1125 | 1147 | 1169 | 1191 | 1213 | 1235 | 1257 | 1279 | 1301 | 1323 | 1345 | 1367 | 1389 | 1411 | 1434 | 1456 | 1478 | 1500
+22.1 mm
per year since 2004 (statistically significant, p < 0.001)
+27%
2020-25 vs 2004-19, versus a normal year-to-year swing of about 16%
33 of 45
independent rainfall series meaningfully wetter. None drier
Notes: Using only the reliable record from 2004, average rainfall across Nepal is rising about 22.1 millimetres a year, and the trend is statistically significant. Recent years, 2020 to 2025, are about 27 percent wetter than 2004 to 2019. Rainfall naturally swings about 16 percent from year to year, so this change is bigger than normal noise. 33 of the 45 independent rainfall series show a meaningful increase; none show a meaningful decrease. One caution: satellite products get reprocessed, so a small part of any trend could be instrumental.

## Slide 6: Extreme-rain days are up by half
CLIMATE | EXTREMES
F2
F3
Chart: Extreme-rain days per district per year (heaviest 5% of rainy days)
| 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Baseline 2004-2019 | 5.8 | 5 | 5.8 | 6.1 | 7 | 5.9 | 6.9 | 7.2 | 5.6 | 8.8 | 6.4 | 5.5 | 4 | 4.7 | 5.4 | 5.8 | 0 | 0 | 0 | 0 | 0 | 0
Recent 2020-2025 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 9.6 | 11.6 | 7.3 | 6.5 | 11.9 | 6.5
6.0 → 8.9
extreme days per district per year (+49%). Borderline significant (p = 0.05)
But 26 August was an ordinary rain day
About 20 mm fell in the corridor that day, below the 29.5 mm extreme threshold. The trigger was ice, not rain: rainfall monitoring alone would have missed it.
Notes: We defined an extreme rain day as one of the heaviest five percent of rainy days for each district, because what counts as extreme in a dry district is different from a wet one. The average district went from 6 to 8.9 extreme days a year, about 49 percent more. The trend is borderline significant, so we call it a strong indication rather than proof. Here is the twist. January to August 2026 was the third wettest on record, but on 26 August itself the corridor got about 20 millimetres, below the extreme threshold. The disaster was triggered by ice collapsing, not by rain. That matters for where we invest.

## Slide 7: Eight districts: extreme terrain on big rivers
TERRAIN AND RIVERS
F4
Chart: Each dot is a district (scores 0-100)
Steep and on major rivers | 78.5 | 78 | 79.9 | 82.4 | 81.3 | 77.7 | 77.8 | 79.4
Top third on both measures
Gorkha
Sankhuwasabha
Ramechhap
Dhading
Mugu
Humla
Rukum West
Kalikot
Why together? Landslides can dam rivers and burst downstream; ice collapses travel down steep valleys through river corridors. Steep plus river means cascading hazard.
Ruggedness = spread of elevation within the district (supplied slope data is corrupted).
Notes: Next, physical geography. Terrain ruggedness is how much the elevation varies inside a district: valleys and peaks together mean steep, unstable ground. River hazard combines how big the river is with how close the land is to it. These two measures are almost unrelated, so each adds new information. Eight districts are in the top third on both, including Gorkha, Sankhuwasabha and Ramechhap. Why does the combination matter? A landslide can block a river and then burst, and an ice collapse travels down steep valleys through river corridors. That cascade is exactly what happened on 26 August.

## Slide 8: Assets cluster in cities; fragility in mountains
EXPOSURE AND VULNERABILITY
F5
F6
Chart: Exposure score: people and critical assets (top 8)
| Kathmandu | Kaski | Lalitpur | Rupandehi | Makwanpur | Parasi | Syangja | Dolakha
Exposure | 100 | 91.2 | 83.3 | 82.5 | 82.4 | 80.5 | 79.7 | 76.7
Chart: Vulnerability score: weak road and hospital access (top 8)
| Taplejung | Darchula | Bajura | Sankhuwasabha | Khotang | Myagdi | Rukum East | Bardiya
Vulnerability | 100 | 99.4 | 82.9 | 82 | 81.9 | 81.1 | 77.8 | 75.1
Kathmandu Valley, Pokhara (Kaski) and the southern plains hold most people. Dolakha holds the most hydropower (587 MW).
One or two mapped hospitals for 100,000+ people and very sparse roads. Not captured: poverty, age, housing quality.
Notes: Exposure is what's in harm's way: people, density, hospitals, schools and hydropower. It concentrates in Kathmandu, Pokhara and the southern plains, plus hydropower hubs like Dolakha. We tested different weights and the ranking barely changed. Vulnerability is how hard it is to cope and to help: we use road density and people per hospital. The most vulnerable districts are remote mountain districts like Taplejung and Darchula. We are honest about what's missing: poverty, age structure and housing quality aren't in the data, so vulnerability is only partly measured.

## Slide 9: High only where all three are high
THE RISK INDEX
HAZARD
Flood: rain + rivers
Landslide: rain + terrain
×
EXPOSURE
People, density, hydropower, hospitals, schools
×
VULNERABILITY
Road access and people per hospital
=
RISK
Geometric mean of the three, scored 0-100
Log scaling
Stops giants like Kathmandu flattening every other district onto the same score
Weights tested
Equal weights give almost the same ranking (ρ = 0.99), so our judgment calls don't drive results
Multiply, don't add
No hazard must mean no risk. An additive version ranks similarly anyway (ρ = 0.90)
Notes: Here is how the index is built. Hazard comes in two versions: flood hazard combines heavy rain with river size and closeness; landslide hazard combines heavy rain with terrain ruggedness. We multiply hazard, exposure and vulnerability using a geometric mean, so a district scores high only if all three are high. If any one is near zero, risk is low. Three choices to know: we log-scaled skewed numbers so Kathmandu doesn't squash everyone else; we checked that our weights don't change the answer; and we chose multiplication because it matches what risk means.

## Slide 10: The ten highest-risk districts
THE RISK INDEX
Chart: Combined risk score (0-100)
| Myagdi | Darchula | Taplejung | Sankhuwasabha | Pyuthan | Bardiya | Gorkha | Kaski | Sunsari | Doti
Risk | 100 | 94.7 | 92.6 | 88.6 | 87.1 | 87 | 85.4 | 81.9 | 81.1 | 80.4
What the top ten share
Steep mountain terrain and heavy rain
Weak road and hospital access
Mostly hill and mountain districts, not the big cities
Where is the 26 Aug corridor?
Sindhupalchok #21, Nuwakot #40, Rasuwa #47 of 77. Our index does not flag it. The validation explains why.
Notes: These are the ten highest-risk districts on the combined index: Myagdi, Darchula, Taplejung, Sankhuwasabha and so on. They combine steep terrain and heavy rain with weak road and hospital access. Notice what's not here: the corridor hit on 26 August. Sindhupalchok ranks 21 and Rasuwa 47. That is an important signal, and the validation section explains it.

## Slide 11: Tested against 12,341 real disasters
VALIDATION
F7
F8
F9
Landslide index
ρ = 0.52
vs recorded landslides
VALIDATED
Terrain ruggedness is the strongest driver; explains about half the variation (R² = 0.49)
Combined index
ρ = 0.39
vs all events (0.43 vs deaths)
MODERATE
Significant and useful, but driven almost entirely by its landslide part
Flood index
ρ = 0.24
vs recorded floods
NOT VALIDATED
Floods happen where our variables don't look. Explained on the next slide
Reading ρ (rank correlation across 77 districts): 0 = no link | 0.3 = weak | 0.5 = moderate | 0.7+ = strong
Notes: This is the most important part. Until now, our index is just a hypothesis. We tested it against 12,341 disasters recorded by Nepal's BIPAD system since 2011, after removing duplicate records. The landslide index works: a correlation of 0.52 with recorded landslides, and terrain ruggedness alone explains about half the difference between districts. The combined index is moderate, around 0.4, but that comes almost entirely from its landslide part. The flood index fails, at only 0.24. We did not re-tune the model to make this number look better; that would be cheating. Instead we found the reason.

## Slide 12: Why the flood index fails: floods are on the plains
VALIDATION | FLOODS
F9
Chart: Correlation with recorded flood events (ρ)
| Flood hazard score | Terrain ruggedness | Road density | Exposure score
rho | -0.08 | -0.26 | 0.32 | 0.38
Most recorded floods
Jhapa, Morang, Kathmandu, Sunsari, Kailali
Mostly flat southern lowlands (Terai), plus Kathmandu Valley: dense, well-connected, low-lying.
The cause: our flood variables describe mountain rivers and rain. Lowland floods happen where rivers leave the mountains and spread over flat, crowded plains. No variable in the data captures floodplain flatness.
We report this rather than re-tuning the model until the number looks good.
Notes: Why do floods fail? Look at where floods are actually recorded: Jhapa, Morang, Sunsari, Kailali, and Kathmandu. Flat southern lowlands, plus Kathmandu. Flood counts go down with rugged terrain and up with population and roads. Our flood hazard score has essentially no link at all. The explanation is a missing variable: we measure mountain rivers and rainfall, but lowland floods happen where rivers spread across flat, crowded plains, and the dataset has nothing on floodplains. Part of it is also reporting: floods get recorded where people and roads are. The brief tells us to explain weak results, not hide them, and that's what we've done.

## Slide 13: Decision: separate flood and landslide indices
METHODOLOGICAL DECISION
Index | vs recorded floods | vs recorded landslides
Combined index | 0.12 | 0.47
Flood index | 0.24 | 0.10
Landslide index | 0.02 | 0.52
Highlighted: the best index for each hazard. Spearman ρ across 77 districts.
1
Floods and landslides strike different places
Their district counts are unrelated (ρ = −0.13). One number can't rank both.
2
Each specific index wins on its own hazard
Landslide 0.52 vs combined 0.47; flood 0.24 vs combined 0.12.
3
A single index would hide a weakness
Its apparent success is its landslide part. Separating shows floods need better data.
Notes: The brief asked us to decide, with evidence, whether one combined index or separate flood and landslide indices is more defensible. The evidence points to separate indices. First, floods and landslides happen in different districts. Second, each specific index beats the combined one on its own hazard. Third, a single number would hide the fact that we predict landslides well and floods poorly. So we use two indices, and we treat the flood index as low confidence.

## Slide 14: The record has blind spots, including this event
VALIDATION | DATA QUALITY
F10
F11
Chart: Recorded disaster events per year (BIPAD)
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
2011-2023 | 464 | 268 | 420 | 162 | 80 | 561 | 569 | 645 | 762 | 943 | 851 | 554 | 825 | 0 | 0 | 0
2024-2026 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1964 | 1362 | 1911
Reporting changed, not disasters
Events quadrupled after 2023 while deaths per event fell from 0.52 to 0.04: many more minor incidents logged
The 26 Aug collapse is missing
Only six minor events and zero deaths are recorded in the corridor afterwards
Glacial risk is invisible to our data
No glacial-outburst records at all. Corridor ranks #21 and #47
Notes: The test also revealed problems with the record itself. Recorded events jump about four-fold after 2023, but deaths per event drop sharply. That means far more small incidents are being logged; it's a reporting change, not four times more disasters. More strikingly, the 26 August collapse that prompted this assessment is not in the record: only six minor events with no deaths in the corridor afterwards. There are no glacial lake outburst records at all. And our index ranks the corridor in the middle of the pack, because glacial hazard simply isn't in the data. These blind spots shape the investment.

## Slide 15: USD 100M: money follows evidence
RECOMMENDATION
Chart: Allocation (USD million)
| Terrain & glacial monitoring | Infrastructure reinforcement | Landslide early warning | Community preparedness | Data infrastructure | Flood early warning
USD M | 22 | 20 | 18 | 15 | 15 | 10
$63M
Act where evidence is strong: landslide and flood early warning, infrastructure, community preparedness
$37M
Close the blind spots that hid this disaster: glacial and terrain monitoring, better disaster and flood data
Notes: Here's the recommendation. The principle is simple: money follows evidence. 63 million goes to direct protection where our analysis is solid: landslide early warning in the validated high-risk districts, flood warning where floods are actually recorded, reinforcing exposed infrastructure, and preparing the most isolated communities. 37 million goes to the blind spots: monitoring glaciers and unstable terrain, including the August corridor, and fixing the disaster and flood data so the next assessment can see what this one could not.

## Slide 16: Every dollar traces to a finding
RECOMMENDATION
Line | USD | Target districts (selected by rule) | Findings
Landslide early warning | $18M | Myagdi, Kaski, Taplejung, Darchula, Pyuthan, Gorkha, Lamjung, Sankhuwasabha | F1, F2, F8
Flood early warning | $10M | Jhapa, Morang, Kathmandu, Sunsari, Kailali | F9
Terrain & glacial monitoring | $22M | Dhading, Gorkha, Humla, Mugu, Ramechhap, Rasuwa, Rukum West, Sankhuwasabha, Sindhupalchok | F3, F4, F8, F11
Infrastructure reinforcement | $20M | Chitwan, Dang, Dhading, Dolakha, Kailali, Kaski, Lamjung, Myagdi, Parasi, Ramechhap, Rasuwa, Solukhumbu, Sunsari, Syangja, Tanahu | F3, F5
Community preparedness | $15M | Taplejung, Darchula, Bajura, Sankhuwasabha, Myagdi, Rukum East, Bardiya, Mugu, Jajarkot, Doti | F6
Data infrastructure | $15M | National, piloted in: Surkhet, Parasi, Parbat, Bardiya, Nawalpur, Mugu, Salyan, Ramechhap, Rukum East, Doti | F9, F10, F11
Notes: Every line is traceable. Landslide early warning goes to the top eight on the validated landslide index. Flood warning goes to the five districts with the most recorded floods, because our flood index failed. Glacial monitoring goes to the high-mountain districts that are steep and on major rivers, plus Sindhupalchok and Rasuwa. Infrastructure reinforcement targets high exposure plus every district with 150 megawatts or more of hydropower. Community preparedness targets the most vulnerable districts, and data infrastructure is national, piloted where hazard is high but few events are recorded. F-numbers refer to the findings in the notebook.

## Slide 17: Three things to remember
IN SUMMARY
1
Rain extremes are rising
+22.1 mm a year since 2004 and about half again as many extreme-rain days.
F1, F2
2
We can rank landslide risk, not floods or glacial collapse
Terrain explains half of landslide variation. Floods and the August collapse sit in data blind spots.
F8 to F11
3
Money follows evidence
$63M protects where evidence is strong; $37M closes the blind spots that hid this disaster.
All findings
Explore the live app: nepal-climate-risk.streamlit.app · Kingsley Chigozie, Analyst · Full method and code: nepal_risk_assessment.ipynb
Notes: Three things to remember. One: rain extremes in Nepal are rising. Two: with this data we can rank landslide risk with reasonable confidence, but floods and glacial collapses like 26 August sit in blind spots. Three: our 100 million follows the evidence, protecting where we're confident and closing the gaps where we're not. Thank you, I'm happy to take questions.

## Slide 18: Sources, assumptions and limitations
APPENDIX
Data sources
NASA POWER (power.larc.nasa.gov): daily rainfall (PRECTOTCORR), temperature, humidity, wind
HydroSHEDS: elevation (15 arc-sec DEM) and flow accumulation
Nepal National Statistics Office, 2021 Census: population and density
OpenStreetMap (Overpass API): hospitals, schools, roads, bridges
Wikipedia, List of power stations in Nepal (9 Mar 2026): hydropower
geoBoundaries ADM2: district boundaries and area
BIPAD Portal, Government of Nepal: disaster incidents 2011-2026
Key assumptions
Climate trends 2004-2025 only; 45 independent series counted once
Extreme day = above district P95 of rainy days (≥ 1 mm)
Baseline 2004-19 vs recent 2020-25; meaningful if larger than baseline year-to-year variation
Ruggedness = elevation standard deviation (slope data unusable)
Skewed variables log-scaled, then min-max to 0-100
Exposure weights 30/20/20/15/15 (population, density, hydropower, hospitals, schools)
Risk = geometric mean of hazard, exposure, vulnerability
Limitations
No poverty, age, housing or early-warning coverage data
OpenStreetMap undercounts rural facilities and roads
One rainfall point per district; coarse satellite grid
No floodplain or glacial-lake variables
Disaster record: reporting surge after 2023; 26 Aug 2026 event missing
Correlation shows association, not cause
Notes: Reference slide for questions: data sources as cited in the data dictionary, every major assumption, and the limitations we identified. The notebook documents each one in detail.